## Slide 1
Introduction
Information Theory is a branch of probability theory which may be applied to the study of the communication systems.
We will study digital communications – using a file (or network protocol) as the channel, Claude Shannon Published a paper in 1948 that was the beginning of the branch of information theory.
Block Diagram of communication system

## Slide 2
Introduction
It deals with the mathematical modelling and analysis of a communication system rather than with the physical sources and physical channels.
Two important elements presented in this theory are
- Binary Source (BS) and Binary Symmetric Channel (BSC).
A binary source is a device that generates one of the two possible symbols ‘0’ and ‘1’ at a given rate ‘r’, measured in symbols per second.
These symbols are called bits (binary digits) and are generated randomly.
The BSC is a medium through which it is possible to transmit one symbol per time unit.

## Slide 3
Introduction
Information theory tries to analyse communication between a transmitter and a receiver through an unreliable channel.
This approach analyse the amount of information produced by the source.
The source information measure, the channel capacity measure and the coding are all related by one of the Shannon theorems stated as:
“If the information rate of a given source does not exceed the capacity of a given channel then there exists a coding technique that makes possible transmission through this unreliable channel with an arbitrarily low error rate”.

## Slide 4
What is information?
Information of an event depends only on its probability of occurrence and is not dependent on its content.
The randomness of happening of an event and the probability of its prediction as a news is known as information.
The message associated with the least likelihood event contains the maximum information.

## Slide 5
Axioms of Information
Information is a non-negative quantity: I (p) ≥ 0.
If an event has probability 1,we get no information from the occurrence of the event:
I (1) = 0.
If two independent events occur (whose joint probability is the product of their individual probabilities).
Then the information we get from observing the events is the sum of the two information: I (p1* p2) = I (p1) + I (p2).
I (p) is monotonic and continuous in p.

## Slide 6
Information Source
An information source may be viewed as an object which produces an event.
The outcome of which is selected at random according to a probability distribution.
The set of source symbols is called the source alphabet and the elements of the set are called symbols or letters.

## Slide 7
Information Source
Information source can be classified as
- Memory & Memoryless.
A source with memory is one for which a current symbol depends on the previous symbols.
A memoryless source is one for which each symbol produced is independent of the
previous symbols.
A discrete memoryless source (DMS) can be characterized by the list of the symbol, the probability assignment of these symbols and the specification of the rate of generating these symbols by the source.

## Slide 8
Information Content of a DMS
The amount of information contained in an event is closely related to its uncertainty.
A mathematical measure of information should be a function of the probability of the outcome and should satisfy the following axioms:
- Information should be proportional to the uncertainty of an outcome
- Information contained in independent outcomes should add up.

## Slide 9
Measure of Information
Let us consider a DMS denoted by ‘x’ and having alphabet {x1, x2, ……, xm}.
The information content of the symbol xi, denoted by I (𝑥𝑖) is defined by
where P(𝑥𝑖) is the probability of occurrence of symbol 𝑥𝑖 .
For any two independent source messages 𝑥𝑖 and 𝑥𝑗 with probabilities 𝑃𝑖 and 𝑃𝑗 respectively and with joint probability P (𝑥𝑖 , 𝑥𝑗 ) = 𝑃𝑖 𝑃𝑗 .
The information of the messages is the addition of the information in each message
𝐼𝑖𝑗 = 𝐼𝑖 + 𝐼𝑗 .
𝐼 (
1
𝑏 𝑃(𝑥𝑖 )
= − log 𝑃(𝑥 )

## Slide 10
Note that I(X 𝑖 ) satisfies the following properties.
        I(X 𝑖 ) = 0 for P(X 𝑖 ) = 1
        I(X 𝑖 ) ≥ 0
3. I(X 𝑖 ) > I(Xj) if P(X 𝑖 ) < P(Xj)
4. I(X 𝑖 , Xj)= I(X 𝑖 ) + I(Xj) if X 𝑖 and Xj are independent
Unit of I (X 𝑖 ): The unit of I (X 𝑖 ) is the bit (binary unit) if b = 2, Hartley or decit if b = 10 and nat (natural unit) if b = e. it is standard to use b = 2.
log2 𝑎 =ln 𝑎/ ln 2 = log 𝑎/ log 2
Measure of Information

## Slide 11
Entropy (Average Information)
Entropy is a measure of the uncertainty in a random variable.
The entropy H, of a discrete random variable X is a measure of the amount of uncertainty associated with the value of X.
For quantitative representation of average information per symbol we make the following assumptions:
    The source is stationary so that the probabilities may remain constant with time.
    The successive symbols are statistically independent and come from the source at an average rate of ‘r’ symbols per second.

## Slide 12
Entropy (Average Information)
3. The quantity H(X) is called the entropy of source X. it is a measure of the average information content per source symbol.
4. The source entropy H(X) can be considered as the average amount of uncertainty within the source X that is resolved by the use of the alphabet.
H(X) = E [I(xi)] = - ΣP(xi) I(xi) = - ΣP(xi)log2 P(xi) b/symbol.

## Slide 13
Properties of Entropy
The source entropy H(X) satisfies the relation: 0 ≤ H(X) ≤ log2 m, where m is the size of the alphabet source X.
  0 ≤ 𝐻(𝑋)≤ log2 ; m = no. of symbols of the alphabet of source X.
2. When all the events are equally likely, the average uncertainty must have the largest value i.e. log2 𝑚≥ 𝐻(𝑋)
3. H (X) = 0, if all the P(xi) are zero except for one symbol with P = 1.

## Slide 14
Information Rate
If the time rate at which X emits symbols is ‘r’ (symbols), the information rate R of the source is given by
R = r H(X) b/s [(symbols / second) * (information bits/ symbol)].
R is the information rate
H(X) = Entropy or average information.

## Slide 15
Applications of Information Theory
Video abstraction – extraction
Secure data transmission
Channel capacity
Speech coding
Waveform coding
Losless data compression
cryptography